## Slide 1: Sistem Terdistribusi IF2222
2022-23 Ganjil
02: Review Networking
Husni

## Slide 2: Sistem Terdistribusi 2022
Mengenal Sistem Terdistribusi
Review Jaringan Komputer (layer 2, 3, dan 4)
Arsitektur Sistem Terdistribusi
Remote Procedure Calls (RPC)
Layanan Penamaan
Sinkronisasi Data (2 pekan)
Message Passing Interface (MPI)
Contoh Arsitektur: Hadoop, Pregel, Blockchain
Teknik Caching
Teknik Replikasi Data (2 pekan)
Basis Data Terdistribusi
Toleransi Kegagalan

## Slide 3: Capaian Pembelajaran
Kuliah ini bertujuan memberikan pemahaman mendalam dan pengalaman langsung tentang:
Prinsip yang menjadi basis dari sistem terdistribusi
Prinsip untuk optimalisasi sistem terdistribusi
Model pemrograman sistem terdistribusi dan mesin analitika
Bagaimana sistem terdistribusi modern memenuhi tuntutan aplikasi terdistribusi kontemporer

## Slide 4: Today…
Last Session:
  Mengenal Sistem Terdistribusi
Today’s Session:
  Network Types
  Networking Principles: Layering, Encapsulation, Routing and Congestion Control
Announcements:

## Slide 5: Learning Outcomes
After two lectures on networks, you will be able to:
  Identify different types of networks
  Describe various networking principles such as layering, encapsulation, and packet-switching, among others
  Examine how packets are routed
  Realize how congestion is controlled
  Analyze the performance, scalability, and reliability of networks

## Slide 6
A distributed system is a collection of components that communicate to solve a problem
Why should designers of distributed systems know about networks?
  Networking issues severely affect performance, fault-tolerance, and security of distributed systems
  E.g., Gmail outage on Sep 1, 2010 – Google Spokesman said “we had slightly underestimated the load which some recent changes placed on the request routers. … . few of the request routers became overloaded… causing a few more of them to also become overloaded, and within minutes nearly all of the request routers were overloaded.”
Networks in Distributed Systems

## Slide 7: A Primer: Latency and Bandwidth
Case 1
Case 2
Case 3
B
L
L
B
L
B = Bandwidth (or Capacity) and L = Latency (or Delay)
B × L gives approximately the number of bits in flight
As B × L increases, uncertainty increases (more bits might get lost)
High value of B × L leads to “Buffer Bloat”
B

## Slide 8
Networking Issue | Comments on a Distributed System Design
Performance
Scalability
Reliability
Security
Mobility
Quality-of-service
Affects choices of whether to optimize for network or other resources
Size of Internet is increasing; expect greater traffic and latency in future
Detect communication errors and perform error-checks at the application layer (end-to-end argument!)
Install firewalls at gateways; deploy end-to-end authentication; employ encryption, etc.,
Expect intermittent connection for mobile devices
Internet is best-effort. It is hard to ensure strict QoS guarantees for, say, multimedia data
Networks in Distributed Systems
Notes: Authentication verifies the identity of a user or a service, and authorization determines their access rights.

## Slide 9
Important ways to classify networks
  Based on size
    Body Area Networks (BAN)
    Personal Area Networks (PAN)
    Local Area Networks (LAN)
    Wide Area Networks (WAN)
  Based on technology
    Ethernet Networks
    Wireless Networks
    Cellular Networks
Network Classification

## Slide 10
Network Classification – BANs and PANs
Body Area Networks (BAN):
  Devices form wearable computing units
  Several Body Sensor Units (BSUs) communicate with Body Central Unit (BCU)
  Typically, low-cost and low-energy networking
Personal Area Networks (PAN):
  PAN connects various digital devices carried by a user (mobile phones, tablets, cameras)
  Low-cost and low-energy networking
  e.g., Bluetooth
Notes: 10
The types of networks can be classified based on size:
Personal Area Networks: Various digital devices carried by the user is connected using a low-cost, low-energy network. e.g. Bluetooth

## Slide 11
Computers connected by single communication medium
  e.g., Twisted copper wire, optical fiber
High data-transfer-rate and low latency
LAN consists of
  Segment
    Usually within a department/floor of a building
    Shared bandwidth, no routing necessary
  Local Networks
    Serves campus/office building
    Many segments connected by a switch/hub
    Typically, represents a network within an organization
Network Classification – LAN
Notes: 11
Local Area Networks: High speed computers connected through a single communication medium (optical, wired or wireless) . “Segment” is a part of the network that is connected by a single medium (e.g. ethernet cable). When a hosts inside a LAN transmits a packet, all other hosts can receive the packet. Hence, there is no need for routing. The bandwidth available is shared between all the hosts. A LAN can be made up of many segments. There is generally a host, which is called as switch or the hub, that helps to connect two or more segments. Communication between hosts in a LAN generally provides high bandwidth and low-delay. But most popularly used LANs, such as Ethernet-based LAN, does not not guarantee bandwidth or delay.

## Slide 12
Generally, covers a wider area (cities, countries,...)
Consists of networks of different organizations
Traffic is routed from one organization to another
  Routers
Bandwidth and latency
  Vary
  Worse than a LAN
Largest WAN = Internet
Network Classification – WAN

## Slide 13
A Point-to-point link
Local Area Network (LAN)
A Segment
A Network
Wide Area Network (WAN)
Brief Summary of Important Networks
(Based on Size)
A network of networks
Notes: 13

## Slide 14
Ethernet Networks
  Predominantly used in the wired Internet
Wireless LANs
  Primarily designed to provide wireless access to the Internet
  Low-range (100s of m), high-bandwidth
Cellular networks (2G/3G/4G/5G)
  Initially, designed to carry voice
  Large range (few kms)
  Low-bandwidth
Types of Networks – Based on Technology

## Slide 15
Network | Example | Range | Bandwidth (Mbps) | Latency (ms)
Wired LAN | Ethernet | 1-2 km | 10 – 10,000 | 1 – 10
Wired WAN | Internet | Worldwide | 0.5 – 600 | 100 – 500
Wireless PAN | Bluetooth | 10 – 30 m | 0.5 – 2 | 5 – 20
Wireless LAN | WiFi | 0.15 – 1.5 km | 11 – 108 | 5 – 20
Cellular | 2G – GSM | 100m – 20 km | 0.270 – 1.5 | 5
Cellular | 3G | 1 – 5 km | 348 – 14.4 | 100 – 500
Cellular | 4G | 16 km | 10- 100 | 36-48
Modern Cellular | 5G | 2 km | 50- 1000 | 10-30
Typical Performance for Different Types of Networks

## Slide 16: Latency and Bandwidth
Case 1
Case 2
Case 3
B
L
L
B
L
B = Bandwidth (or Capacity) and L = Latency (or Delay)
B × L gives approximately the number of bits in flight
As B × L increases, uncertainty increases (more bits might get lost)
High value of B × L leads to “Buffer Bloat”
B
(Ethernet)
(WiFi)
(WAN)

## Slide 17
Network Protocols
Packet Transmission
Network Layers
  Physical layer
  Data-link layer
  Network layer and routing
  Transport layer and congestion control
Networking Principles

## Slide 18
If two entities want to communicate on a network, pre-defined agreements are necessary
  How a message will be formatted?
  How does the receiver know the last bit in the message?
  How can a receiver detect if the message is damaged?
“Protocol” is a well-known set of rules and formats to be used for communication between the entities
Standardizing a well-known set of protocols supports communication among heterogeneous entities
Networking Protocols
Notes: Networks allow an entity on one machine to communicate with another entity on another machine

## Slide 19
Messages are broken up into packets
  A packet is the unit of data that is transmitted between an origin and a destination
  Packets can be of arbitrary lengths
Maximum size of the packet is known as Maximum Transmission Unit (MTU)
  MTU prevents one host from sending a very long message
Each packet has two main fields
  Header: Contains meta-information about the packet
    e.g., Length of the packet, receiver ID
  Data
Header
Data
Packet Transmission

## Slide 20: Network Layers
Network software is arranged into a hierarchy of layers
  Protocols in one layer perform one specific functionality
  Layering is a scalable & modular design for complex software
Typical functionalities in a network software:
011100011 0011 011
Dest
Src
P1
P3
P2
Destination machine
Functionality | Layer
Transmits bits over a transmission medium
Coordinates transmissions from multiple hosts that are directly connected over a common medium
Routes the packets through intermediate networks
Handles messages – rather than packets – between sender and receiver processes
Satisfies communication requirements for specific applications
Physical
Data link
Network
Transport
Application

## Slide 21: OSI Reference Model
Open Systems Interconnection (OSI) Reference Model
  A layered networking model standardized by ISO
  The model identifies various layers and their functionalities
Functionality | Layer | Example Protocols
Satisfy communication requirements for specific applications | Application | HTTP, FTP
Transmit data in network representation that is independent of representation in individual computers | Presentation | CORBA data representation
Support reliability and adaptation, such as failure detection and automatic recovery | Session | SIP
Handle messages – rather than packets – between sender and receiver processes | Transport | TCP, UDP
Route the packet through intermediate networks | Network | IP, ATM
Coordinate transmissions from multiple hosts that are directly connected over a common medium | Data-link | Ethernet MAC
Transmit bits over a transmission medium | Physical | Ethernet

## Slide 22: Packet Encapsulation
Encapsulation is a technique to pack and unpack data packets in a layered architecture

## Slide 23: Layers that We Will Study Today
Physical layer
Data-link layer
Network layer
Transport layer

## Slide 24: Layers that We Will Study Today
Physical layer
Data-link layer
Network layer
Transport layer

## Slide 25: Physical Layer
Physical layer protocols transmit a sequence of bits over a transmission medium
  Modulate the bits into signals that can be transmitted over the medium
Transmission Medium | Type of signal transmitted
Twisted-pair (Ethernet cable) | Electrical signal
Fiber Optic Circuits | Light signal
Wireless channel | Electro-magnetic signal
A physical layer protocol
Data-link layer protocol
Transmission Medium
Bits
Signal

## Slide 26: Layers that We Will Study Today
Physical layer
Data-link layer
Network layer
Transport layer

## Slide 27: Data-link Layer
Protocols in data-link layer ensure that the packets are delivered from one host to another within a local network
Data-link layer protocols provide two main functionalities:
  How to coordinate between the transmitters such that packets are successfully received?
    Coordination
  How to identify another host on the local network?
    Addressing over local networks

## Slide 28: Coordination at Data-link Layer
A packet is not received successfully at the receiver if a sender transmits the data when another sender’s transmission is active
  The packet is said to have experienced collision if it is not successfully received at the receiver
Collision is avoided by sensing the medium before transmission

## Slide 29: Addressing over Local Networks
Each device that is connected to a network has a unique address called Medium Access Control (MAC) address
  MAC addresses are six bytes long
    e.g., 2A:D4:AB:FD:EF:8D
Approach:
  Data-link layer broadcasts the packet over the medium
  Receiver reads the packet header and checks if the packet is addressed to it
x
x

## Slide 30: The Four Layers We Are Studying
Physical layer
Data-link layer
Network layer
Transport layer

## Slide 31: Network Layer
Network layer protocols perform the role of routing
  They ensure that a packet is routed from the source machine to the destination machine
  Packets may traverse different LANs to reach the destination
Internet Protocol (IP) is a widely-used network layer protocol
  IP addresses are typically used to identify machines
Destination
Source
Router

## Slide 32: Router
A router is a device that forwards the packets between multiple networks
Routers are connected to two or more networks
  Each network interface is connected to a LAN or a host
Packet travels up until the network layer on the router
LAN-3
Int-3
Int-2
A Router
LAN-2
LAN-1
Physical
Data-link
Network
Transport
Application
Source machine
Physical
Data-link
Network
Transport
Application
Dest machine
Physical
Data-link
Network
Router
Int-1

## Slide 33: Routing Algorithm
Packets have to be transmitted in a series of hops through the routers
  The series of hops that a packet takes is known as a route
Routing algorithm is responsible for determining the routes for the transmission of packets
Challenges for designing routing algorithms in the Internet:
  Performance: The traffic across different networks vary
  Router failures: Routers in the Internet may fail
S
D
R1
R2
R4
R4

## Slide 34: Routing Algorithm (Cont’d)
Routing algorithms have two activities
  Determine the next-hop taken by each packet
    The algorithm should be fast and efficient
  Dynamically update connectivity information
    Maintain the knowledge of the network by monitoring routers and traffic
The above activities are distributed throughout the network
  Routing decisions are made on an hop-by-hop basis
  Information about possible next-hop routers is stored locally
  Information is updated periodically
Let us study a simple routing algorithm called “Distance Vector Algorithm”

## Slide 35: Distance Vector Algorithm
Distance Vector (DV) relies on graph theory to find the best route in a given network
  It uses a well-known shortest path algorithm called Bellman-Ford
Two activities for the DV routing algorithm:
  Determining the best next-hop at each router
  Dynamically update connectivity information at all the routers

## Slide 36: Distance Vector Algorithm – Next-hop Determination
Each router maintains a routing table that consists of:
  Destination: The destination IP of the packet
  Link: The outgoing link on which the packet should be forwarded
  Cost: The distance between the router and the destination
    E.g., Cost can be estimated as the delay for the packet to reach the destination
Router looks up the table to determine the best next-hop
Routing table at a router A
To
Link
Cost
A
B
C
D
E
local
1
1
3
1
0
1
2
1
2
A
B
D
1
3
Links
Routers
Hosts or local networks
C
2
E
4

## Slide 37: Routing Tables for an Example Scenario
A
B
E
D
C
1
2
3
4
6
5
Routers
Hosts or local networks
Links
Routings from A
Routings from B
Routings from C
To
Link
Cost
To
Link
Cost
To
Link
Cost
A
B
C
D
E
local
1
1
3
1
0
1
2
1
2
A
B
C
D
E
1
local
2
1
4
1
0
1
2
1
A
B
C
D
E
2
2
local
5
5
2
1
0
2
1
Routings from D
Routings from E
To
Link
Cost
To
Link
Cost
A
B
C
D
E
3
3
6
local
6
1
2
2
0
1
A
B
C
D
E
4
4
5
6
local
2
1
1
1
0

## Slide 38: Distance Vector Algorithm – Updating the Connectivity Information
Connectivity is updated by exchanging routing table
Router Information Protocol (RIP) is used for sending update messages
  Send routing table to neighboring routers
    Periodically, or when local table changes
  When a neighbor’s routing table is received:
Case | If the received routing table … | Updates to the local routing table
1 | Has a new destination that is not in the local routing table | Update the Cost and Link
2 | Has a better-cost route to a destination in the local routing table | Update the Cost
3 | Has a more recent information | Update the Cost and Link

## Slide 39
Pseudocode for RIP
Send: Each t seconds or when Tl changes, send Tl on each non-faulty outgoing link
Receive: Whenever a routing table Tr is received on link n:
for all rows Rr in Tr {
if (Rr.link != n) {
Rr.cost = Rr.cost + 1; // Update cost
Rr.link = n; // Update next-hop
if (Rr.destination is not in Tl) {
add Rr to Tl; // add new destination to Tl
}
else for all rows Rl in Tl {
if (Rr.destination = Rl.destination) {
// Rr.cost < Rl.cost : remote node has better route
// Rl.link = n : information is more recent
if (Rr.cost < Rl.cost OR Rl.link = n) {
Rl = Rr;
}
}
}
}
}
A
B
E
D
C
1
2
3
4
6
5
Routing table at router A
To
Link
Cost
A
D
local
3
0
1
Tl at A
C
3
3
Routing table of router B
To
Link
Cost
A
B
local
1
1
0
C
2
1
Tr recvd @ A from B on link n=1
Case 1
Case 2
Case 3
Notes: 39
Ask:
What happens when a link is broken?
Will this surely converge even if link breaks?
How can you take care of link-quality? Say link A-B is 10Gbps Ethernet link and link A-C is 2Mbps wireless link.

## Slide 40: Summary: Routing over Internet
Each machine over the Internet is identified by an IP Address
Source machine transmits the packet over its local network
Intermediate routers examine the packet, and forward it to the best next-hop router
If the destination is directly attached to the local network of a router, the router forwards the packet over the respective local network
Routers exchange information to keep an up-to-date information about the network

## Slide 41: Layers that we will study today
Physical layer
Data-link layer
Network layer
Transport layer

## Slide 42: Transport Layer
Transport layer protocols provide end-to-end communication for applications
This is the lowest layer where messages (rather than packets) are handled
Messages are addressed to communication ports attached to the processes
  Transport layer multiplexes each
  packet received to its respective port
P1
P3
P2
Transport layer protocol
Destination machine
Network layer protocol

## Slide 43: Simple Transport Layer Protocols
Simple transport protocols provide the following services:
  Multiplexing Service
  Connection-less Communication: The sender and receiver processes do not initiate a connection before sending the message
    Each message is encapsulated in a packet (also called as datagram)
    Messages at the receiver can be in different order than the one sent by the sender
    E.g., User Datagram Protocol (UDP)

## Slide 44: Advanced Transport Layer Protocols
Advanced transport layer protocols typically provide more services than simple multiplexing
Transmission Control Protocol (TCP) is a widely-used protocol that provides three additional services:
  Connection-oriented Communication
  Reliability
  Congestion Control

## Slide 45: 1. Connection-Oriented Communication
Sender and receiver will handshake before sending the messages
  Handshake helps to set-up connection parameters, and to allocate resources at destination to receive packets
Destination provides in-order delivery of messages to the intended process
  Destination will buffer the packets until previous packets are received
  It will then deliver packets to the process in the order that the sender had used
P1
P3
P2
TCP protocol
Destination machine
P1
P3
P1
TCP protocol
Source machine
Shall I send?
OK. Start sending

## Slide 46: 2. Reliability
Packets may be lost in the network due to buffer overflows at the router or transmission error(s)
In TCP, destination sends an ACK to the sender
  If ACK is not received at the sender, the sender will infer a packet error, and retransmit the packet

## Slide 47: 3. Congestion Control
The capacity of a network is limited by the individual communication links and routers
  Limited buffer space and link-bandwidth
What happens if a source transmits packets at a rate that is greater than the capacity of the network?
  Packets drop at intermediate routers
  Corresponding ACKs will NOT be received at the source
  The source retransmits
  More packets build-up on the router queue
  The network collapses

## Slide 48: 3. Congestion Control (Cont’d)
To avoid congestion, two functionalities can be adopted
  Detect congestion at routers
    If a router expects a buffer overflow, it typically follows one of two strategies:
      It drops packets and lets sources regulate upon observing packet losses
      It sends an “Explicit Congestion Notification (ECN)” packet to sources
  Regulate input at sources
    If the TCP-sender concludes congestion (e.g., it receives an ECN packet), then it reduces its sending rate
Notes: What is the best layer for congestion control?
Do you know any other protocol similar to TCP that is widely used?
When/where is congestion control important, where is it not?

## Slide 49: Recap: Learning Objectives
You will identify how computers over the Internet communicate
Specifically, after the two lectures in networking you will be able to:
  Identify different types of networks
  Describe networking principles such as layering, encapsulation, and packet-switching
  Examine how packets are routed and how congestion is controlled
  Analyze scalability, reliability, and fault-tolerance over the Internet

## Slide 50: Next Class
Arsitektur Sistem Terdistribusi